## Slide 1: Control robots using Javascript through Cylon.js
Presented By : The Assembly Team
WiFi:- In5 Tech
Pass:- WelcomeToIn5

## Slide 2: Getting started
Things to install:
NodeJS
Cylon.js
Arduino IDE
Code editor (Visual studio code/ Sublime Text)

## Slide 3: DEMO

## Slide 4: Things to do
Introduction to Nodejs and Cylonjs
Working with Cylonjs and a keyboard
Blinking LED on Arduino
Servos
Using a keyboard to control the servos

## Slide 5: NodeJS
Open source server environment
Uses Javascript
What can it be used for?
Web application frameworks
Access to wide variety of packages via npm

## Slide 6: Cylon.js
A Javascript framework
What can it be used for?
Commanding robots
Internet of things

## Slide 7: Cylon.js
To install Cylon.js
Using the terminal:
npm install cylon
npm install cylon-firmata cylon-gpio cylon-i2c
To use Cylon.js with the keyboard:
npm install cylon cylon-keyboard

## Slide 8: Detecting keyboard input
"use strict";
var Cylon = require('cylon');
Cylon.robot({
//main code here
}).start();
Setting up requirements
The “main” method

## Slide 9: Detecting keyboard input
connections: {
keyboard: { adaptor: 'keyboard' }
},
devices: {
keyboard: { driver: 'keyboard' }
},
Defining the connections (NOTE: CHANGE THE PORT)
Defining the devices

## Slide 10: Detecting keyboard input
work: function(my) {
my.keyboard.on('a', function(key) {
console.log("a pressed");
});
}
Prints ‘a pressed’ when the a key is pressed

## Slide 11: Detecting keyboard input
"use strict";
var Cylon = require('cylon');
Cylon.robot({
connections: {
keyboard: { adaptor: 'keyboard' }
},
devices: {
keyboard: { driver: 'keyboard' }
},
work: function(my) {
my.keyboard.on('a', function(key) {
console.log("a pressed");
});
}
}).start();

## Slide 12: Detecting keyboard input
To run the script using terminal:
node keyboard.js

## Slide 13: Now for the hardware…

## Slide 14: Arduino
A programmable microcontroller
What can it be used for?
Internet of Things
Controlling lights/sensors/motors

## Slide 15: Servo motor
A rotary or linear actuator that allows for precise control of angular and linear position.

## Slide 16: Uploading Firmata

## Slide 17: Blinking LED

## Slide 19: Servos with Cylon.js
"use strict";
var Cylon = require('cylon');
Cylon.robot({
//main code here
}).start();
Setting up requirements
The “main” method

## Slide 20: Servos with Cylon.js
connections: {
arduino: { adaptor: 'firmata', port: 'COM3' }
},
devices: {
servo: { driver: 'servo', pin: 3 }
},
Defining the connections (NOTE: CHANGE THE PORT)
Defining the devices

## Slide 21: Servos with Cylon.js
work: function(my) {
var angle = 0 ;
my.servo.angle(angle);
every((1).second(), function() {
angle = angle + 180 ;
if (angle > 180) {
angle = 0
}
my.servo.angle(angle);
});
}
Making the servos rotate left to right every second

## Slide 22
var Cylon = require("cylon");
Cylon.robot({
connections: {
arduino: { adaptor: 'firmata', port: 'COM3' }
},
devices: {
servo: { driver: 'servo', pin: 3 }
},
work: function(my) {
var angle = 0 ;
my.servo.angle(angle);
every((1).second(), function() {
angle = angle + 180 ;
if (angle > 180) {
angle = 0
}
my.servo.angle(angle);
});
}
}).start();

## Slide 23: Servos with Cylon.js
To run the script using terminal:
node servos.js
Make sure “Standard Firmata” has been uploaded on the Arduino
“npm install cylon-firmata cylon-gpio cylon-i2c”

## Slide 24: Controlling servos with the keyboard
"use strict";
var Cylon = require('cylon');
Cylon.robot({
//main code here
}).start();
Setting up requirements
The “main” method

## Slide 25: Controlling servos with the keyboard
connections: {
arduino: { adaptor: 'firmata', port: 'COM3' },
keyboard: { adaptor: 'keyboard' }
},
devices: {
servo1: { driver: 'servo', pin: 3, connection: "arduino" },
keyboard: { driver: 'keyboard', connection: "keyboard" }
},
Defining connections and devices

## Slide 26: Controlling servos with the keyboard
work: function(my) {
var angle1 = 0 ; my.servo1.angle(angle1);
my.keyboard.on("a", function() {
if (angle1 == 0){
angle1 = 180;
my.servo1.angle(angle1);
} if (angle1 ==180) {
angle1 = 0;
my.servo1.angle(angle1);
}
});
}
Rotates the servos when the “a” key is pressed

## Slide 27
"use strict";
var Cylon = require('cylon');
Cylon.robot({
// change the port below to match whatever your Arduino is actually plugged into
connections: {
arduino: { adaptor: 'firmata', port: 'COM3' },
keyboard: { adaptor: 'keyboard' }
},
devices: {
servo1: { driver: 'servo', pin: 3, connection: "arduino" }, keyboard: { driver: 'keyboard', connection: "keyboard" }
},
work: function(my) {
var angle1 = 0 ; my.servo1.angle(angle1);
my.keyboard.on("a", function() {
if (angle1 == 0){
angle1 = 180;
my.servo1.angle(angle1);
} if (angle1 ==180) {
angle1 = 0;
my.servo1.angle(angle1);
}
});
}
}).start();

## Slide 28: Run the code

## Slide 29: Now try it with 3 servos! :)

## Slide 30: THANK YOU